## JSON configuration
190917, updated 17.9.2019/pekka
We specify hardware configuration as JSON and then generate the C file automatically by Python. Simple case: WORK_LIGHT binary output turns on the lights. The example IO application is called “jane” and example hardware it runs on is named “carol” (ESP32 development board).

- The WORK_LIGHT output is mapped to specific IO pin by gpio pin number, or bank number and pin number within bank. We may also have some attributes for IO pin. For example LIGHT_SWITCH input could have sensing speed to filter out very short pulses, etc. For analog input, PWMs, etc, there can be a lot of parameters.
- So one pin (or more generally IO item since we can include timers etc), is configured by set of attribytes, name, type, address and various parameters. For example a digital output WORK_LIGHT is at address 3 of bank 1, or digital input LIGHT_SWITCH is address 2 of bank 4 using filtering speed 3.
- An IO pin is “input”, “output”, “analoginput”...
- Pin attributes are “bank”, “addr”, “speed”...
- Attribute values excluding group are always integers.
- Some parameters can be changed while the code runs, like speed.

As JSON this pin setup would look something like:

{
  "pins": {
    "name": "jane",
    "title": "IO pin setup for 'jane' application on 'carol' hardware",
    "inputs": {
 "LIGHT_SWITCH": {"bank": 4, "addr": 2, "speed": 3},
 "GARAGE_DOOR_SWITCH": {"bank": 1, "addr": 5}
    },
    "outputs": {
 "WORK_LIGHT": {"bank": 1, "addr": 3, "group": "MYLIGHTS"},
 "NIGHT_LIGHT": {"bank": 1, "addr": 5, "group": "MYLIGHTS"}
    },
    "analog_inputs": {
 "TEMPERATURE_SENSOR": {"bank": 2, "addr": 2, "speed": 3, "delay": 11}
    }
  }
}