## Generating C source and header files from JSON
190917, updated 2.11.2019/pekka
The hardware specific IO configuration, like jane-io.json, is converted to C files by pins-to-c.py script. This will generate jane-io.c and jane-io.h file, which can be compiled into the application.

jane-io.h
/* This file is gerated by pins-to-c.py script, do not modify. */
OSAL_C_HEADER_BEGINS
typedef struct
{
  struct
  {
    PinGroupHdr hdr;
    Pin dip_switch_3;
    Pin dip_switch_4;
    Pin touch_sensor;
  }
  inputs;
  struct
  {
    PinGroupHdr hdr;
    Pin led_builtin;
  }
  outputs;
  struct
  {
    PinGroupHdr hdr;
    Pin potentiometer;
  }
  analog_inputs;
  struct
  {
    PinGroupHdr hdr;
    Pin servo;
    Pin dimmer_led;
  }
  pwm;
}
pins_t;
extern const IoPinsHdr pins_hdr;
extern const pins_t pins;
OSAL_C_HEADER_ENDS

And in C file
/* This file is gerated by pins-to-c.py script, do not modify. */
#include "pins.h"
static os_short pins_inputs_dip_switch_3_prm[]= {PIN_PULL_UP, 1};
static os_short pins_inputs_touch_sensor_prm[]= {PIN_TOUCH, 1};
static os_short pins_analog_inputs_potentiometer_prm[]= {PIN_SPEED, 3, PIN_DELAY, 11};
static os_short pins_pwm_servo_prm[]= {PIN_RESOLUTION, 12, PIN_FREQENCY, 50, PIN_INIT, 2048};
static os_short pins_pwm_dimmer_led_prm[]= {PIN_RESOLUTION, 12, PIN_FREQENCY, 5000, PIN_INIT, 0};
const pins_t pins =
{
  {{3, &pins.inputs.dip_switch_3},
    {"dip_switch_3", PIN_INPUT, 0, 34, pins_inputs_dip_switch_3_prm, sizeof(pins_inputs_dip_switch_3_prm)/sizeof(os_short), OS_NULL},
    {"dip_switch_4", PIN_INPUT, 0, 35, OS_NULL, 0, OS_NULL},
    {"touch_sensor", PIN_INPUT, 0, 4, pins_inputs_touch_sensor_prm, sizeof(pins_inputs_touch_sensor_prm)/sizeof(os_short), OS_NULL}
  },
  {{1, &pins.outputs.led_builtin},
    {"led_builtin", PIN_OUTPUT, 0, 2, OS_NULL, 0, OS_NULL}
  },
  {{1, &pins.analog_inputs.potentiometer},
    {"potentiometer", PIN_ANALOG_INPUT, 0, 25, pins_analog_inputs_potentiometer_prm, sizeof(pins_analog_inputs_potentiometer_prm)/sizeof(os_short), OS_NULL}
  },
  {{2, &pins.pwm.servo},
    {"servo", PIN_PWM, 0, 32, pins_pwm_servo_prm, sizeof(pins_pwm_servo_prm)/sizeof(os_short), OS_NULL},
    {"dimmer_led", PIN_PWM, 1, 33, pins_pwm_dimmer_led_prm, sizeof(pins_pwm_dimmer_led_prm)/sizeof(os_short), OS_NULL}
  }
};
static const PinGroupHdr *pins_group_list[] =
{
  &pins.inputs.hdr,
  &pins.outputs.hdr,
  &pins.analog_inputs.hdr,
  &pins.pwm.hdr
};
const IoPinsHdr pins_hdr = {pins_group_list, sizeof(pins_group_list)/sizeof(PinGroupHdr*)};