## JSON configuration
190917, updated 2.11.2019/pekka
The idea is to write application’s hardware configurations as JSON, and then generate matching C code and header files by Python script pins-to-c.py. It is possible to write directly C code, writing JSON just makes it easier because information needs to be written only in one place.

For example I have application “jane”, which controls “led_builtin” binary output to on a LED on IO board. I want to test this on hardware I named “carol”, which is ESP32, Arduino libraries and the LED connected to pin 2. I need to bind pin address 2 and other pin attributes (like pull-up), etc to name “led_builtin”. I write this information a JSON file jane/config/pins/carol/jane-io.json. Then I run the pins-to-c.py script to generate C code. I use same JSON file together with IOCOM signal configuration JSON to map the IO pins to IOCOM communication signals.

If I would need to run same “jane” application on different hardware, let’s say “alice”: Separate JSON HW configuration file would written for it.

- The LED_BUILTIN output is mapped to specific IO pin by pin number, and/or bank number and. We may also have some attributes for IO pin. For example SERVO PWM has frequency, resolution, initial value, etc.
- One pin, or more generally IO item since we can include timers etc, is configured by name, address and and various parameters.
- Group attribute can be used to generate groups of pins.
- Attribute values excluding group are integers.
- Some parameters can be changed while the code runs.
- IO pins can be mapped directly to IOCOM signals.

As JSON this pin setup would look something like:

{
  "io": [{
    "name": "jane",
    "title": "IO pin setup for 'jane' application on 'carol' hardware",
    "groups": [
      {
        "name": "inputs",
        "pins": [
        {"name": "dip_switch_3", "addr": 34, "pull-up": 1},
        {"name": "dip_switch_4", "addr": 35},
        {"name": "touch_sensor", "addr": 4, "touch": 1}
        ]
      },
      {
        "name": "outputs",
        "pins": [
        {"name": "led_builtin", "addr": 2}
        ]
      },
      {
        "name": "analog_inputs",
        "pins": [
        {"name": "potentiometer", "addr": 25, "speed": 3, "delay": 11, "max": 4095}
        ]
      },
      {
        "name": "pwm",
        "pins": [
        {"name": "servo", "bank": 0, "addr": 32, "frequency": 50, "resolution": 12, "init": 2048, "max": 4095},
        {"name": "dimmer_led", "bank": 1, "addr": 33, "frequency": 5000, "resolution": 12, "init": 0, "max": 4095}
        ]
      }
    ]
  }]
}

Note: Min and max can be used to set range of values. These do not effect anything to IO, but allow the hardware configuration JSON to pass these values to application.