# Introduction
190916, updated 16.9.2019/pekka
The “pins” library separates IO application from hardware level IO functions, so the same IO application can be run on different micro-controllers or as Linux/Windows simulation. This library is optional and not integal part of iocom library: Any other IO library can be used instead. Typically IO hardware accessed tough the “pins” interface are GPIO, ADC/DAC, PWM, timers, etc.
## About “pins” library
Function of the "pins" library is to:
- Provide an application with hardware independent access to GPIO, analogs, PWM, timers, etc.
- Provide subs to call forward hardware dependent IO library, like pigpio on Raspberry PI, HAL on STM32, IO simulation on PC and so forth.
- Define hardware pin configuration in such way that it needs to be written only once, and is then available from C code, memory maps and in documentation.

Some taughts
- Hardware specific IO headers are not included in application (except when there is need to bypass "pins").
- Hardware addresses, etc. need to be mapped to application at some point. This could be simply written as one C file. But we write it as JSON and then generate the C file automatically by Python script. This enable using the PIN information to automate documentation, IOCOM memory mapping, etc.