## Generating C source and header files from JSON
190917, updated 17.9.2019/pekka
The hardware specific IO configuration is stored in JSON file, like jane-io.json. Running cpins.sh script will generate a C source files, which can be then compiled with the application.

jane-io.h
OSAL_C_HEADER_BEGINS
extern const Pin jane_LED_BUILTIN;
extern const Pin jane_POTENTIOMETER;
extern const Pin jane_DIP_SWITCH_4;
extern const Pin jane_TOUCH_SENSOR;
extern const Pin jane_DIP_SWITCH_3;
extern const Pin jane_DIMMER_LED;
extern const Pin jane_SERVO;
extern const Pin *jane_pins;
OSAL_C_HEADER_ENDS

And in C file
#include "pins.h"
const Pin jane_LED_BUILTIN = {"LED_BUILTIN", PIN_OUTPUT, 0, 2, OS_NULL, 0, OS_NULL, OS_NULL};
static os_short jane_POTENTIOMETER_prm[]= {PIN_DELAY, 11, PIN_SPEED, 3};
const Pin jane_POTENTIOMETER = {"POTENTIOMETER", PIN_ANALOG_INPUT, 0, 25, jane_POTENTIOMETER_prm,
sizeof(jane_POTENTIOMETER_prm)/sizeof(os_short), OS_NULL, &jane_LED_BUILTIN};
const Pin jane_DIP_SWITCH_4 = {"DIP_SWITCH_4", PIN_INPUT, 0, 35, OS_NULL, 0, OS_NULL, &jane_POTENTIOMETER};
static os_short jane_TOUCH_SENSOR_prm[]= {PIN_TOUCH, 1};
const Pin jane_TOUCH_SENSOR = {"TOUCH_SENSOR", PIN_INPUT, 0, 4, jane_TOUCH_SENSOR_prm,
sizeof(jane_TOUCH_SENSOR_prm)/sizeof(os_short), OS_NULL, &jane_DIP_SWITCH_4};
static os_short jane_DIP_SWITCH_3_prm[]= {PIN_PULL_UP, 1};
const Pin jane_DIP_SWITCH_3 = {"DIP_SWITCH_3", PIN_INPUT, 0, 34, jane_DIP_SWITCH_3_prm,
sizeof(jane_DIP_SWITCH_3_prm)/sizeof(os_short), OS_NULL, &jane_TOUCH_SENSOR};
static os_short jane_DIMMER_LED_prm[]= {PIN_FREQENCY, 5000, PIN_RESOLUTION, 12, PIN_INIT, 0};
const Pin jane_DIMMER_LED = {"DIMMER_LED", PIN_PWM, 1, 33, jane_DIMMER_LED_prm,
sizeof(jane_DIMMER_LED_prm)/sizeof(os_short), OS_NULL, &jane_DIP_SWITCH_3};
static os_short jane_SERVO_prm[]= {PIN_FREQENCY, 50, PIN_RESOLUTION, 12, PIN_INIT, 2048};
const Pin jane_SERVO = {"SERVO", PIN_PWM, 0, 32, jane_SERVO_prm, sizeof(jane_SERVO_prm)/sizeof(os_short), OS_NULL, &jane_DIMMER_LED};

const Pin *jane_pins = &jane_SERVO;

WARNING: Python 3.6 or newer is needed to preserve dictionary order. If run with older versions, IO pins in C are not in same order as in this C file, which can cause problems down the road since linked list order is may be used to give pins addresses is iocom memory block.