## JSON configuration
190917, updated 17.9.2019/pekka
We specify hardware configuration as JSON and then generate the C file automatically by shell script cpins.sh. The cpins.sh calls python script /coderoot/pins/scripts/pins-to-c/pins-to-c.py.

Simple case: LED_BUILTIN binary output turns on the build in LED on IO board. The example IO application is called “jane” and example hardware it runs on is named “carol” (ESP32 development board).

- The LED_BUILTIN output is mapped to specific IO pin by GPIO pin number, or bank number and pin number within bank. We may also have some attributes for IO pin. For example SERVO PWM has frequency, resolution, initial value, etc.
- So one pin (or more generally IO item since we can include timers etc), is configured by name, address and and various parameters.
- Group attribute can be used to generate groups of pins.
- Attribute values excluding group are always integers.
- Some parameters can be changed while the code runs.

As JSON this pin setup would look something like:
{
  "pins": {
    "name": "jane",
    "title": "IO pin setup for 'jane' application on 'carol' hardware",
    "inputs": {
 "DIP_SWITCH_3": {"addr": 34, "pull-up": 1},
 "DIP_SWITCH_4": {"addr": 35},
 "TOUCH_SENSOR": {"addr": 4, "touch": 1}
    },
    "outputs": {
 "LED_BUILTIN": {"addr": 2}
    },
    "analog_inputs": {
 "POTENTIOMETER": {"addr": 25, "speed": 3, "delay": 11, "max": 4095}
    },
    "pwm": {
 "SERVO": {"bank": 0, "addr": 32, "frequency": 50, "resolution": 12, "init": 2048, "max": 4095},
 "DIMMER_LED": {"bank": 1, "addr": 33, "frequency": 5000, "resolution": 12, "init": 0, "max": 4095}
    }
  }
}