## Pins example “jane”
190918, updated 18.9.2019/pekka
The “jane” is name for “pins” library example IO device application. “Carol” is name for a specific IO board, here MELIFE ESP32 development board which has specific uses for it’s pin.
### Carol hardware
It is useful to give name to a IO board so it can be called. My breadboard MELIFE ESP32 test is called “carol”, so the name “carol” means ESP32 with Arduino libraries. This combination can be developed by either Visual Studio Code + Platform IO or Arduino IDE.

“Carol” is a bit of a mess, it is needs only to survive for a day of testing

Carol hardware wiring is as follows:

IO pin name	IO pin type	IO address	Description
DIP_SWITCH_3	digital input	34	Blue 8 dip switch block, switch pin 3 grounds the input. Dip switch is also declared as pull-up, but this doesn't seem to do anything on ESP32.
DIP_SWITCH_4	digital input	35	Blue 8 dip switch block, switch pin 4 grounds the input.
TOUCH_SENSOR	digital input	4	Touch the sensor T0 (GPIO4)
POTENTIOMETER	analog input	25	10k potentiometer wired to give voltage from 0 to 3.3V, ADC channel 8
SERVO	PWM	22	Servo PWM control. PWM channel 0 (set as bank) is used with 50 Hz frequency and 12 bits precision, and initialized at middle (2048)
DIMMER_LED	PWM	33	LED dimmer PWM control. PWM channel 1 (set as bank) is used with 5000 Hz frequency and 12 bits precision, and initialized at dark (0)

The IO pin name is name what Jane application uses for specific functionality, like potentiometer, DIP switch 3, or PWM controlled dimmed blue led. IO address is hardware specific, that tells what has been wired to which pin of the ESP32. For Arduino libraries, it is Arduino GPIO pin number.

### JSON configuration
Hardware specification is written in jane-io.json.

{
  "pins": {
    "name": "jane",
    "title": "IO pin setup for 'jane' application on 'carol' hardware",
    "inputs": {
    "DIP_SWITCH_3": {"addr": 34, "pull-up": 1},
    "DIP_SWITCH_4": {"addr": 35},
    "TOUCH_SENSOR": {"addr": 4, "touch": 1}
    },
    "outputs": {
    "LED_BUILTIN": {"addr": 2}
    },
    "analog_inputs": {
    "POTENTIOMETER": {"addr": 25, "speed": 3, "delay": 11, "max": 4095}
    },
    "pwm": {
    "SERVO": {"bank": 0, "addr": 32, "frequency": 50, "resolution": 12, "init": 2048, "max": 4095},
    "DIMMER_LED": {"bank": 1, "addr": 33, "frequency": 5000, "resolution": 12, "init": 0, "max": 4095}
    }
  }
}

Min and max can be used to set range of values. These do not effect anything to IO, but allow the hardware configuration JSON to pass these values to application. So if same application is compiled for different hardwares, it can adopt to HW capabilities/settings.
### Generating C code to access IO
The C code jane-io.c and jane-io.h can then be generated, and will contain information from the JSON file. Script /coderoot/pins/examples/jane/pins/carol/cpins.sh will generate the C files.

jane-io.h

OSAL_C_HEADER_BEGINS
extern const Pin jane_DIP_SWITCH_3;
extern const Pin jane_DIP_SWITCH_4;
extern const Pin jane_TOUCH_SENSOR;
extern const Pin jane_LED_BUILTIN;
extern const Pin jane_POTENTIOMETER;
extern const Pin jane_SERVO;
extern const Pin jane_DIMMER_LED;
extern const Pin *jane_pins;
OSAL_C_HEADER_ENDS

jane-io.c

#include "pins.h"
const Pin jane_DIP_SWITCH_3 = {"DIP_SWITCH_3", PIN_INPUT, 0, 34, OS_NULL, 0, OS_NULL, OS_NULL};
const Pin jane_DIP_SWITCH_4 = {"DIP_SWITCH_4", PIN_INPUT, 0, 35, OS_NULL, 0, OS_NULL, &jane_DIP_SWITCH_3};
static os_short jane_TOUCH_SENSOR_prm[]= {PIN_TOUCH, 1};
const Pin jane_TOUCH_SENSOR = {"TOUCH_SENSOR", PIN_INPUT, 0, 4,jane_TOUCH_SENSOR_prm, sizeof(jane_TOUCH_SENSOR_prm)/sizeof(os_short), OS_NULL, &jane_DIP_SWITCH_4};
const Pin jane_LED_BUILTIN = {"LED_BUILTIN", PIN_OUTPUT, 0, 2, OS_NULL, 0, OS_NULL, &jane_TOUCH_SENSOR};
static os_short jane_POTENTIOMETER_prm[]= {PIN_SPEED, 3, PIN_DELAY, 11};
const Pin jane_POTENTIOMETER = {"POTENTIOMETER", PIN_ANALOG_INPUT, 0, 25, jane_POTENTIOMETER_prm, sizeof(jane_POTENTIOMETER_prm)/sizeof(os_short), OS_NULL, &jane_LED_BUILTIN};
static os_short jane_SERVO_prm[]= {PIN_FREQENCY, 50, PIN_RESOLUTION, 12, PIN_INIT, 2048};
const Pin jane_SERVO = {"SERVO", PIN_PWM, 0, 32, jane_SERVO_prm, sizeof(jane_SERVO_prm)/sizeof(os_short), OS_NULL, &jane_POTENTIOMETER};
static os_short jane_DIMMER_LED_prm[]= {PIN_FREQENCY, 5000, PIN_RESOLUTION, 12, PIN_INIT, 0};
const Pin jane_DIMMER_LED = {"DIMMER_LED", PIN_PWM, 1, 33, jane_DIMMER_LED_prm, sizeof(jane_DIMMER_LED_prm)/sizeof(os_short), OS_NULL, &jane_SERVO};
const Pin *jane_pins = &jane_DIMMER_LED;
### The jane application
The jane-example.c is simple single thread example IO device application. It demonstrates how to use IO trough “pins” interface.
- The pins_setup() initialize the IO pins.
- pin_set() set IO pin state
- pin_get() get IO pin state

#include "jane.h"
/* Here we include hardware specific IO code. The file name is always same for jane, but
   pins/<hardware> is added compiler's include paths
 */
#include "jane-io.c"
os_timer t;
os_boolean state;
os_int dip3, dip4, touch, dimmer, dimmer_dir, potentiometer;
os_int osal_main(
    os_int argc,
    os_char *argv[])
{
    pins_setup(jane_pins, 0);
    os_get_timer(&t);
    state = OS_FALSE;
    dip3 = dip4 = touch = -1;
    dimmer = 0;
    dimmer_dir = 1;
    potentiometer = -4095;
    /* When emulating micro-controller on PC, run loop. Just save context pointer on
       real micro-controller.
     */
    osal_simulated_loop(OS_NULL);
    return 0;
}
osalStatus osal_loop(
    void *app_context)
{
    os_int x, delta;
    os_char buf[32];
    /* Digital output */
    if (os_elapsed(&t, 50))
    {
        os_get_timer(&t);
        state = !state;
        pin_set(&jane_LED_BUILTIN, state);
    }
    /* Digital input */
    x = pin_get(&jane_DIP_SWITCH_3);
    if (x != dip3)
    {
        dip3 = x;
        osal_console_write(dip3 ? "DIP switch 3 turned ON\n" : "DIP switch 3 turned OFF\n");
    }
    x = pin_get(&jane_DIP_SWITCH_4);
    if (x != dip4)
    {
        dip4 = x;
        osal_console_write(dip4 ? "DIP switch 4 turned ON\n" : "DIP switch 4 turned OFF\n");
    }
    /* Touch sensor */
    x = pin_get(&jane_TOUCH_SENSOR);
    delta = touch - x;
    if (delta < 0) delta = -delta;
    if (delta > 20)
    {
        touch = x;
        if (touch)
        {
        osal_console_write("TOUCH_SENSOR: ");
        osal_int_to_string(buf, sizeof(buf), touch);
        osal_console_write(buf);
        osal_console_write("\n");
        }
    }
    /* Analog input */
    x = pin_get(&jane_POTENTIOMETER);
    delta = potentiometer - x;
    if (delta < 0) delta = -delta;
    if (delta > 100)
    {
        potentiometer = x;
        osal_console_write("POTENTIOMETER: ");
        osal_int_to_string(buf, sizeof(buf), potentiometer);
        osal_console_write(buf);
        osal_console_write("\n");
    }
    /* PWM */
    dimmer += dimmer_dir;
    if (dimmer > 4095 || dimmer < 0) dimmer_dir = -dimmer_dir;
    pin_set(&jane_DIMMER_LED, dimmer);
    return OSAL_SUCCESS;
}

### What was point of all this complexity, why not call Arduino IO directly?
The goal here is to separate IO device application from specific hardware. If we have many somewhat complex IO boards, there is no need to rewrite all software every time hardware or development tool changes. Second goal is to be able to run IO board application as PC simulation. This is quite useful for developing more complex applications with long life time.
This level of abstraction makes sense only in specific environment. In simple cases, one is probably better off calling hardware specific IO direly from application and something like “pins” library is just unnecessary complexity.