## JSON configuration
190917, updated 27.3.2020/pekka
The idea is to write application’s hardware configurations as JSON, and then generate matching C code and header files by Python script pins-to-c.py. It is possible to write directly C code, writing JSON just makes it easier because information needs to be written only in one place.

For example I have application “jane”, which controls “led_builtin” binary output to on a LED on IO board. I want to test this on hardware I named “carol”, which is ESP32, Arduino libraries and the LED connected to pin 2. I need to bind pin address 2 and other pin attributes (like pull-up), etc to name “led_builtin”. I write this information a JSON file jane/config/pins/carol/jane-io.json. Then I run the pins-to-c.py script to generate C code. I use same JSON file together with IOCOM signal configuration JSON to map the IO pins to IOCOM communication signals.

If I would need to run same “jane” application on different hardware, let’s say “alice”: Separate JSON HW configuration file would written for it.

- The led_builtin output is mapped to specific IO pin by pin number, and/or bank number and. We may also have some attributes for IO pin. For example SERVO PWM has frequency, resolution, initial value, etc.
- One pin, or more generally IO item since we can include timers etc, is configured by name, address and and various parameters.
- Group attribute can be used to generate groups of pins.
- Attribute values excluding group are integers.
- Some parameters can be changed while the code runs.
- IO pins can be mapped directly to IOCOM signals.

A JSON pin setup would look something like ESP32 example below:

{
  "io": [{
    "name": "jane",
    "title": "IO pin setup for 'jane' application on 'carol' hardware",
    "groups": [
      {
        "name": "inputs",
        "pins": [
          {"name": "gazerbeam", "addr": 39, "interrupt": 1},
          {"name": "dip_switch_3", "addr": 34, "pull-up": 1},
          {"name": "dip_switch_4", "addr": 35},
          {"name": "touch_sensor", "addr": 36, "touch": 1}
        ]
      },
      {
        "name": "outputs",
        "pins": [
          {"name": "led_builtin", "addr": 33}
        ]
      },
      {
        "name": "analog_inputs",
        "pins": [
          {"name": "potentiometer", "addr": 26, "max": 4095}
        ]
      },
      {
        "name": "pwm",
        "pins": [
          {"name": "servo", "bank": 0, "addr": 22, "frequency": 50, "resolution": 12, "init": 2048, "max": 4095},
          {"name": "dimmer_led", "bank": 1, "addr": 27, "frequency": 5000, "resolution": 12, "init": 0, "max": 4095}
        ]
      },
      {
        "name": "uart",
        "pins": [
          {"name": "U2_TXD", "addr": 17},
          {"name": "U2_RXD", "addr": 16}
        ]
      },
      {
        "name": "debugger",
        "pins": [
            {"name": "AD1_TDI", "addr": 12},
            {"name": "AD0_TCK", "addr": 13},
            {"name": "AD3_TMS", "addr": 14},
            {"name": "AD2_TDO", "addr": 15},
            {"name": "U0_TXD", "addr": 1},
            {"name": "U0_RXD", "addr": 3}
          ]
      },
      {
        "name": "devboard",
        "pins": [
            {"name": "DEV_SCK", "addr": 6},
            {"name": "DEV_SDO", "addr": 7},
            {"name": "DEV_SDI", "addr": 8},
            {"name": "DEV_SHD", "addr": 9},
            {"name": "DEV_SWP", "addr": 10},
            {"name": "DEV_CSC", "addr": 11}
          ]
      }
    ]
  }]
}

### Configuring inputs
Inputs are configured within “inputs” group. Pin name is can be up to 15 characters + terminating ‘\0’. Use only ‘a’ - ‘z’, ‘A’ - ‘Z’, ‘0’ - ‘1’ and underscore ‘_’ characters. The pin name will be used in C code as written. Address “addr” is GPIO pin address.

The attributes for inputs
- pull-up: Set 1 to enable pull-up resistor on input.
- pull-down: Set 1 to enable pull-down resistor on input.
- touch: Set 1 to define this input as touch sensor (this is set up here, even signal may be analog):
- interrupt: Set 1 to trigger HW interrupt when pin state changes, either falling edge, rising edge or both. Edge on which to trigger is in C code.

Examples
          {"name": "gazerbeam", "addr": 39, "interrupt": 1},
          {"name": "dip_switch_3", "addr": 34, "pull-up": 1},

### Configuring outputs
Configuring outputs under “outputs” group is similar to configuring inputs.

The attributes for inputs
- pull-up: Set 1 to enable pull-up resistor on output.
- pull-down: Set 1 to enable pull-down resistor on output.

Example
          {"name": "led_builtin", "addr": 33}

### Configuring analog inputs
Analog inputs are configured within “analog_inputs” group.

The attributes for analog inputs
- addr: GPIO pin address.
- max: Set maximum value for analog input. Typically set by number AD conversion resolution, 1023 for 10-bit ADC and 4095 for 12 bit ADC, etc. Application and IOCOM link can use this setting to scale value to known units, which is useful if for example newer version of the hardware has higher ADC resolution.

Example
          {"name": "potentiometer", "addr": 26, "max": 4095}

### Configuring analog outputs
Analog outputs are configured within “analog_outputs” group.

The attributes for analog outputs
max: Set maximum value for analog output. Typically set by number D/A conversion resolution, 1023 for 10-bit DAC and 4095 for 12 bit DAC, etc.

Example
          {"name": "myaout", "addr": 25, "max": 4095}

### Configuring PWM
PWM pins are configured within “pwm” group.
The attributes for PWM pin
- bank: PWM channel.
- addr: GPIO pin address.
- frequency: PWM frequency in Hz, max 65535.
- frequency-kHz: PWM frequency kHz. This is used instead of “frequency” to set higher frequencies than 65kHz.
- resolution: Number of bits in PWM signal. If set to 12, values range from 0 to 4095. For example 2048 would mean that pin is on 50% of time (50% duty cycle). If generating clock pulse, set 1 bit.
- max: Set maximum value for analog output. Typically set by number D/A conversion resolution, 1023 for 10-bit DAC and 4095 for 12 bit DAC, etc.
- init: Set initial value. for example 1024 with 12 bit resolution would mean 25% duty cycle.

Example
          {"name": "servo", "bank": 0, "addr": 22, "frequency": 50, "resolution": 12, "init": 2048, "max": 4095},
          {"name": "ccd_clock",  "bank": 0, "addr": 22, "timer": 0, "frequency-kHz": 10000, "resolution": 1}

ESP32 notes
- LED PWM of the ESP32 is composed of 16 independent channels (0 .. 15), with configurable duty cycles and wave periods. The accuracy of the duty cycle can be configured up to 16 bits of resolution. Channels 0 … 7 are high speed channels, and 8 … 15 are low speed channels.
- ESP32: ESP32/Arduino implementation ignores “timer” attribute.

### Configuring SPI bus
SPI buses are configured within “spi” group.

The attributes for SPI bus
- addr: SPI bus number to configure.
- max: Set maximum value for analog output. Typically set by number D/A conversion resolution, 1023 for 10-bit DAC and 4095 for 12 bit DAC, etc.
- miso: Sets GPIO pin address for MISO (master in, slave out) signal.
- mosi: Sets GPIO pin address for MOSI (master out, slave in)signal.
- sclk: Sets GPIO pin address for SCLK (clock) signal.
- cs: Sets GPIO pin address for CS (chip select) signal. This enables a specific SPI device.
- dc: Needed for some devices, like some TFT displays. Sets data control GPIO pin address.

Example
          {"name": "tft_spi", "addr": 0, "miso": 19, "mosi": 23, "sclk": 18, "dc": 2}

### Configuring timers
Timers are used to trigger timed interrupts.

Timer attributes
- bank: .
- addr:
- timer: Timer number ?
- frequency: PWM frequency in Hz, max 65535.
- frequency-kHz: PWM frequency kHz. This is used instead of “frequency” to set higher frequencies than 65kHz.

Example
          {"name": "igc_timer",  "bank": 0, "addr": 0, "timer": 0, "frequency-kHz": 250, "resolution": 1},

### Configuring UARTS
Serial port UARTS are configured same way regardless of signal levels, difference between TTL level, RS232, RS422.

UART attributes
- addr: UART number.
- rx: Receive data GPIO pin address.
- tx: Transmit data GPIO pin address.
- tc: Transmit control GPIO pin address (reserved for future).
- speed: Baud rate, divided by 100. Set for example 96 for 9600 bps.

Example
          {"name": "uart2", "addr": 2, "rx": 16, "tx": 17, "speed": 96}

### Configuring pins reserved for debugger and development board
These are skipped by pins-to-c.py script and cannot be accessed from C code. Reason for these to be defined here is to avoid accidentally using a reserved pin, and in future to include these in IO documentation once we have automatic JSON configuration to document converter written.