## Generate 1 MHz clock signal with ESP32
200324, updated 25.3.2020/pekka
### Code
Self standing example code for ESP32, uses esp-idf platform.

/* Example: Generate 1 MHz clock signal with ESP32, note 24.3.2020/pekka
   ESP32: LEDC peripheral can be used to generate clock signals between
   40 MHz (half of APB clock) and approximately 0.001 Hz.
   Please check the LEDC chapter in Technical Reference Manual.

   Example code below.
 */
 include "driver/ledc.h"
 include "driver/periph_ctrl.h"
 void set_1MHz_clock_on_GPIO2(void)
 {
   periph_module_enable(PERIPH_LEDC_MODULE);

   // Set up timer
   ledc_timer_config_t ledc_timer = {
     // We need clock, not PWM so 1 bit is enough.
     .duty_resolution = LEDC_TIMER_1_BIT,

     // Clock frequency, 1 MHz, high speed
     .freq_hz = 1000000,
     .speed_mode = LEDC_HIGH_SPEED_MODE,
     .timer_num = LEDC_TIMER_0,

     // I think not needed for new esp-idf software, try uncommenting
     // .clk_cfg = LEDC_USE_APB_CLK
   };

   ledc_timer_config(&ledc_timer); // Set up GPIO PIN

   ledc_channel_config_t channel_config = {
     .channel = LEDC_CHANNEL_0,
     .duty = 1,
     .gpio_num = 2, // GPIO pin
     .speed_mode = LEDC_HIGH_SPEED_MODE,
     .timer_sel = LEDC_TIMER_0
   };

   ledc_channel_config(&channel_config);
 }

### Scope
The 1 MHz clock pulse on scope display.